## Slide 1: PHTA Discussion
August 20, 2024

## Slide 2: Introduction
Alice Isley, REHS, CPO
P.O. Box 101
Atlantic Beach, NC 28512
252-947-2579
AliceinPKS@gmail.com
Currently working as a private consultant
Previous Experience:
30 years as a Public Health Regulator:
10 years at the county level (Rockingham County, NC)
15 years as a NC State Regional Environmental Health Specialist
5 years as Program Manager for the Public Pool Program
Experience in Los Angeles conducting compliance inspections in early 90’s.

## Slide 3: Disclaimer
I no longer have any regulatory authority or responsibility.
I am prohibited from any activity which would be perceived as service to the state for 6 months following retirement.
This presentation is solely to promote my business as a private consultant.
The information I am giving today is my opinion only, and based on previous experience and/or regulatory documents available to the public.

## Slide 4: NCAC 18A .2521
Stair tread heights should be uniform, any deviation should be done on the lowest tread, in the deepest water.
Based on newly released opinion from the state, the sun shelf is considered a step and the adjustment should be made at the bottom tread (+/- 2 inches)
Uneven stairs can cause trips and falls. The human brain expects manmade stairs to be uniform. Making the adjustment at the lowest tread allows the bather to have the least impact because of being partially submerged in the water.

## Slide 5: NCAC 18A .2539 Emergency Pump Stops
There is no rule in NCAC 18A .2500 to require the use of an emergency stop button
This is not one of the secondary methods to prevent bather entrapment if it requires human intervention.
If used, recommend installation at 52 inches which is the highest it can be located and still be consistent with ADA guidelines.
Building code enforcement of pool related items not consistent; ADA lifts, pressure testing of piping, cut-off switches.
From a Google search:
Emergency stop buttons are required for public or guest use swimming pools and spas by the National Electrical Code (NEC). These buttons should be installed in commercial settings like hotels and motels, but they can also be installed in non-commercial or residential settings as a best practice.
Emergency shutoff switches should also be provided to disconnect power to air blowers, jet system pumps, and recirculation. These switches should be within sight of the pool or spa, easily accessible, and at least 5 feet horizontally from the pool or spa's inside walls.

## Slide 6: NCAC 18A .2522 Deck width requirements
The deck width requirements have been the same since inception of the rules in 1993.
When written, most of the NC rules had some basis in either other regulatory jurisdictions or guidance provided by other agencies.
This guidance has been applied to islands and peninsula widths, see Declaratory Ruling dated July 7, 2006
Decks provide not only emergency access, but also allow for seating. Larger pools = higher bather loads.

## Slide 7: Handrails on Sun Shelves
Recent position from DHHS is at least one handrail is required to enter the pool.
This can be either on a set of traditional stairs, or a single handrail from the deck to the sun shelf.
The 10 foot separation applies to the stairs joining the sun shelf to the deeper water.

## Slide 8: Code Variations between Counties
Counties are allowed to create a local ordinance which is more restrictive than State regulations.
Wake has had a local ordinance for many years. Not likely to change.
They cannot change or eliminate state or Federal requirements.
i.e. Counties cannot by local ordinance eliminate VGB safety requirements, reduce deck minimum sizes, allow certain design components such as vanishing edge pools.
Some differences are caused by building inspection jurisdiction, staffing, etc.

## Slide 9: Introducing new technology to NC Inspectors
Allowing vs. Introducing?
Adoption in rules?
How to change rules:
1. Periodic rule revisions (Slow but best)
2. Declaratory ruling or contested case ruling (Risky for both parties)
3. Session Law / lobbying (Fast but not always adequate/complete)
What crosses over to Building Code?
Introducing new technology
Most counties do not have funding to send staff to conventions
District Ed meetings would probably allow presentations
Eastern District PHA, EHS Symposium allows private sponsors with information booths
Discussion example: Emergency phones moving forward- Next steps

## Slide 10: Getting plans approved on time
Sealed properly- Can sit on a desk for several weeks before being sent back.
Complete and correct
  Include ALL required information
    List emergency equipment and phone location
    Show all required depth and No Diving tiles
    Include details about SOFA configurations include Manufacturers installation info if needed
    Show all pipe sizes ad where sizes change
    Provide correct model numbers, Flow meters sized for return pipe size, etc., 2017 SOFA specs
  Remove any information not relevant to the project
    No spa signage listed for pools
    No vacuum detail if no dedicated vacuum line
    Extra drain/sump information, details
    Incorrect pump curves

## Slide 11
Most plans are denied because:
1. incorrect information has been provided;
2. Needed information has not been included.
Discussion Point: Phone installation on Rooftop casino pool
If you are in a hurry or the local health department charges for resubmittals, consider a pre-submittal plan review.
Includes completed calculations sheet provided for submittal with plans,
Review of design details for compliance,
Completed DSDS for RDP review and sealing if requested,
Consultation with RDP if changes are recommended.
Q & A with county staff if questions or concerns

## Slide 12
For renovations, consider getting advice up front
Discussion: Pool operator drained and installed a Neptune Benson Aegis Shield to avoid consultation fees.
Drain costs (Around $1800) plus install, cost to drain and refill large pool.
Visit to pool after the installation revealed that the new drain cover was not necessary.
Consultation fees would have been $100-$200
Consultation report would have recommended re-piping in the equipment room involving a handful of PVC fittings and a stick of pipe, less than an hour of labor and no draining of pool.

## Slide 13
QUESTIONS?
Alice Isley, REHS, CPO
P.O. Box 101
Atlantic Beach, NC 28512
252-947-2579
AliceinPKS@gmail.com